Easy and safe plug-in. From the distribution box to the device.

The RST family is growing and offering even more possibilities.

The success story continues: With the launch of the safe RST connectors series, WIELAND revolutionized outdoor electrical installation. Now, the company has further expanded the RST product group. The Classic series is expanded by a 7-pole version. Effective immediately, new miniature connectors with a diameter smaller of 15 mm are now available.

Easy, fast and safe - The RST installation philosophy

With the RST product group, WIELAND offers an integrated pluggable installation system, from the distributor to the device. It enables a comprehensive network of electrical connection technology components, all prefabricated and tested in the factory. The huge flexibility of the system as well as its quick and safe assembly significantly increase the operational readiness of plants. Already upon installation, assembly time is reduced by 80%. In case of usage changes, the installation is simple and easily adapted. Defective devices can be replaced like child's play.

RST 20i7 – More poles for greater demands

The requirements for the functionality of luminaires are constantly increasing. In many application areas, luminaires, for example, are required to be dimmable or capable of being operated from ever longer distances. For these increased demands, Wieland is now expanding the existing RST Classic series with a 7-pole version.

The new RST 20i7 is also available with an optional water-stop function, which prevents any penetrated water from continuing along and causing damage to the entire installation. The leaky part is isolated and can be purposefully repaired.

A total of three codings ensure both mechanical and color differentiation of the various circuits. Mechanical coding means that only the male/female pairs that belong together can be inserted, and with the correct polarity. To increase safety, a distinction is drawn between applications with and without protective earth. The compact connectors with key data 250/400V; 600V UL/CSA, 20A, IP 66/68 (3m;2h), 69 offer high modularity and adaptability to the requirements of the application.

In terms of connection technology, users basically have a selection between screw and crimp technology. As an interface to electrical devices, the system offers straight and angled adapters for all standard housing bores (for M16, M20, M25). All devices can therefore easily be converted to RST without changing tools.

WIELAND is a system supplier and naturally supports customers in planning.

RST MICRO – Miniature connectors for LED luminaires and signals

With the advent of LED technology, illumination has changed and gained in importance, particularly in outdoor areas. There is now a whole host of innovative luminaires available. Connecting electrical installations have to meet increased requirements for these new modern luminaires.

Wieland Electric is responding to these new requirements, launching the RST MICRO, a miniature connector, specially designed for LED luminaires and signals. The 2 to 3-pole connector with a diameter of less than 15 mm is optimized for the interface between voltage or current sources and LED modules.

Like the RST 20i7, the RST miniature connector is also available with an optional water-stop feature.

For more information, see www.wieland-electric.com

(x,xxx including spaces)

Wieland RST Connector Family

Background information

Wieland Electric was founded in 1910 in Bamberg and is the inventor of the safe electrical connection technology. The product range includes well over 20,000 components for industrial automation and building installation/automation. With its gesis® system Wieland has led the world in the field of pluggable electrical installation for buildings for over 30 years now. The podis® power bus system is tailored for automation solutions. This modular system is particularly suitable for the effective decentralized installation of logistics and transport facilities. The international family business has subsidiaries and sales organizations in Argentina, Belgium, Canada, China, the Czech Republic, Denmark, France, Germany, Great Britain, Italy, the Philippines, Poland, Romania, Russia, Spain, and the USA, and is represented in over 70 countries. In addition to Wieland Electric GmbH, STOCKO Contact GmbH & Co. KG has been part of the Wieland Group since 1998. Wieland Electric has been certified according to the quality and environmental management systems ISO 9001:2008, EN ISO 14001 as well as the EU Eco-Management and Audit Scheme (EMAS).

PR Contact

Wieland Electric GmbH

Roland Gagel

Marketing

Brennerstraße 10 – 14

96052 Bamberg, Germany

Email:		presse.de@wieland-electric.com

Internet:		www.wieland-electric.com